## Slide 1: Differential Drive (DD)
Project by Stépane BINON
16/08/2025

## Slide 2: NEXT TASKS
Command encoders and nucleo boards, desing for test bench, start learning about FOC
Videos.
  https://www.youtube.com/watch?v=RNRjC5iBhJE
  https://www.youtube.com/watch?v=hxK5hNAsVH0&list=PLbGlpmZLQWJceSkQv96j-L4YyuxS-E0Wm&index=4
  https://chatgpt.com/g/g-p-68a0ae6b37d08191956af3703a806f26/c/68a88881-2538-8321-a30d-66c523741801

## Slide 3: Specifications
Environment:
  Tiled flor/flat surface, must be able to climb 20° slope, must be able to cross a 1cm gap without issues
Capacities:
  With 2 wheels, 5kg of charge
  Full speed at 1.1m/s (10% marge)
  Acceleration => 1m/s in 0.5m at full acceleration => 2m/s² of minimal acceleration
Control:
  Using position, speed or torque for each wheel

## Slide 5: Schema of hardware

## Slide 7: TIMERS
ARR: Auto-Reload Value

## Slide 8: 6 steps

## Slide 9: Step 1: Field-Oriented Control
In a std ESC, the torque is not constant => FOC solves that => Can be seen using a slow rotating motor
Std EXC causes noise due to spike in the current shape (use an oscillosope to see it)
Std ESC is less efficient. FOC « pull » the magneet at the right time (ie torque is maximal) which ensure max efficiency => NEED POSITION.
Standard ESC: only 6 space vectors
FOC ESC: much more space vectors => almost continous

## Slide 11
Motor alignement
Rampe en BO pour mise a 500RPM
Lecture des capteurs (64kHz) avec HRTIM
  Securité en function du courant et de la tension
  Lecture de la BEMF pour determiner la position du rotor

## Slide 13: STM32

## Slide 14: Motors: KAVAN Brushless motor C3542-1250 and ODRIVE
ODrive Motors — ODrive Documentation 0.6.11 documentation
Dual Shaft Motor - D5065 270kv – ODrive Robotics US
Dimensions will be based on this motor to ensure performances during the French Robotic Cup.

## Slide 15
Our driver must be able to take:
Electrical frequency
85A during 3s
65A continously => seems to be way to much, thus, we will limit ourselves to (45+65)/2=55A => We will need to control power consumption
32V

## Slide 16
MOTOR NOISE
Must be absorbed

## Slide 17: Mosfet: NVMFS5C604NLAFT1G
I_d = Drained Current (depend of cooling)
R_ds = Drain to Source Resistance
V_ds = Dran to Source Tension
Q_g: charge for on/off => affect speed
Rise/fall time and delays
Q_oss: charge for Output Capacitance Coss
Qg charge for the gate

## Slide 18
https://www.youtube.com/watch?v=86S-CEXImzU&pp=0gcJCR0AztywvtLA

## Slide 19
https://www.youtube.com/watch?v=_r0xtaYMjYQ

## Slide 20
https://www.youtube.com/watch?v=VgHOHcWu7-U

## Slide 21
General law for LDO

## Slide 22
Mosfet behaviour due to inductance
Protection
Issue

## Slide 23
t_r = rise time => for the 2: <50ns if Rds<80V
t_f = fall time

## Slide 25
How to choose the PWM frequency ?
It can be set afterward

## Slide 26
How does current rise inside the MOSFET+Motor loop ? Must I be warry of 85A for 3s ???
What does it mean ? => PWM impact on current ripple

## Slide 27
How to not burn anything ???
-> Current must be checked at any time and limited

## Slide 28
MOSFET SELECTED: NVMFS5C604NLAFT1G
To take with water flanks
We will need little cooling

## Slide 29
Using 10V fpor the gate results in a faster switching but a higher R_ds
On va prendre 10V

## Slide 31: Gate driver

## Slide 32: Gate driver: MP1922GV-Z
Idea behind the gate driver to send more that
Note, driver do not exactly do this better (no losses, independent)
Sizing: https://community.infineon.com/t5/Knowledge-Base-Articles/Estimating-the-important-parameters-of-a-gate-Gate-driver/ta-p/816852?nobounce

## Slide 34: Chosen
Thus, R_ds is 0.97 (typ) and 1.2 (max). Lets take 1.085 ohm.
To STM32
Power
STM32
MOSFETs control
Sensors and reference
Drain
Gate
Source

## Slide 35
Can be linked for auto restart
Deactivate CS
Deactivate CS
How to process a fault
We need a strat taking into account the 3 GD
SR to define, 10komh should be fine
For 10V => Qg=110nC
Cboot = 880nF
Cboot = 1000nF = 1*µF

## Slide 36
I_fs=100A and V_shunt=50mV => R_shunt=0.5mOhm
R9=R10=R11=1.5mOhm
CSR = GND
50mV*x=3.3
thus 3.3/50*1000=66 => R_csg = 30kOhm (G=52.5)
FS = Full Scale

## Slide 37: 4mm bullet connector

## Slide 38: Resistors

## Slide 40
https://www.youtube.com/watch?v=7gz98K_hCEM

## Slide 43: TAGS to use
To remove duplicated code at linking time
  -ffunction-sections
  -fdata-sections
  -Wl,--gc-sections,--icf=all

## Slide 44
CNN pas trop dur -> En une heure
Data synthetique
Bien rechercher pour les datasets
Analyse de l’homogenité du dataset (biais du au nombre de chaque erreur)
DATABASE
Pas de continual learning mais automatization de la detection de vrai classes de défaut (attention au taux d’erreur)
Note = note*defaut classe differentes Yolo en premiere etape ULTRALITICS, detect super rapidement
Supprimer des couches lors de l’entrainenment pour la robustesse (dropout)

## Slide 45: VOCAB ANGLAIS
Hard sledding: dur/parcours du combattant. Sledding -> luge: parcours glissant
Design an algorithm absorbedly: desginer un algorithm de maniere approfondie

## Slide 46: Ressources
Understand kV: Understanding KV Rating in Brushless Motors – HobbyGradeRC.com
Motor List and info: ODrive motor guide - Google Sheets
Encoders List and info: ODrive encoder guide - Google Sheets
Video on basics of FOC: (33) What is FOC? (Field Oriented Control) And why you should use it! || BLDC Motor – YouTube
Matlab FOC control: Field-Oriented Control (FOC) - MATLAB &amp; Simulink
Designing the MBLDC, a Custom ESC and BLDC Driver: Designing the MBLDC, a custom ESC and BLDC driver – Maakbaas
Thermal vias: How Thermal Vias Dissipate Heat in PCBs | Sierra Circuits
Cool analogy for capacitor: https://www.youtube.com/watch?v=KSylo01n5FY
Design of a 5V regulator, simple video: https://www.youtube.com/watch?v=d-j0onzzuNQ
Good motor enclosure and tuto about FOC: https://www.youtube.com/watch?v=AmS22zwl2EA
Gate driver working principle: https://www.youtube.com/watch?v=YeUbmOKi0Q4 (total tutos: https://www.youtube.com/playlist?list=PLbGlpmZLQWJceSkQv96j-L4YyuxS-E0Wm)
Phil’s LAB: STM32 with Kicad (https://www.youtube.com/watch?v=nkHFoxe0mrU)
Back-EMF explanation: https://mechtex.com/blog/back-emf-in-bldc-motors-a-complete-guide
Detailed pdf on sensorless control using BackEMF: https://www.nxp.com/docs/en/application-note/AN1913.pdf
Completition with FOC of previous source: https://www.nxp.com.cn/docs/en/application-note/AN1930.pdf
STM32 tuto: https://www.youtube.com/watch?v=dnfuNT1dPiM
C code deployment MatLab : https://www.youtube.com/watch?v=LAcnV_5GruY
FOC controller: https://www.youtube.com/watch?v=e0sQnVmE7DU
STM32 on 6 steps: https://wiki.st.com/stm32mcu/wiki/STM32MotorControl:6-step_Firmware_Algorithm
STM32 from bare metal, advanced principles: https://www.youtube.com/watch?v=7xnUsPo_fG8

## Slide 47: Definitions and Acronyms List

## Slide 48: Ressources FOC control
Pich detection using an egg: https://www.youtube.com/shorts/0jK4JGhhrNY
Control torque: https://www.youtube.com/shorts/SaAPLW2w2H0
Simple DIY BLDC: https://www.youtube.com/shorts/Ujhx4hHET3U

## Slide 49: Annexes